## Slide 1: IPM FOR food service staff
Lesson 2 of 2
Self-Guided Education Module

## Slide 2: Learning Objectives
Describe key elements of inspection and monitoring
    What to look for
    Where to look
    Tools used
    Frequency
Describe key elements of sanitation and exclusion
    Strategies
    Tactics
    Tools

## Slide 3: Learning Objectives
Describe proper and thorough cleaning procedures for:
    Drain areas
    Floors
    Corners
    Beneath equipment
    Floor joints

## Slide 4: Learning Objectives
Explain the importance of effective communication, education and cooperation between
    Food service staff
    Custodial staff
    Maintenance staff
    Facility managers
    Administrators

## Slide 5
In the previous lesson, you learned how to identify common pests in kitchens and pantries
In this lesson, you will learn how to keep pests under control using a combination of techniques that you already use in your daily work!
Food Service Staff and IPM
Cleaned, dried dishes ready for the next mealtime – Shujuan Li, University of Arizona

## Slide 6
Do What You Already Do, Just Think About Pests!
Food service staff can play an important role in educating and influencing other school staff and students on how to avoid pest-conducive conditions
Food service professionals show clean handling of cut fruit using gloves and covered containers
- DC Central Kitchen
Prepared food is kept covered till serving time

## Slide 7
What to look for:
Pests
Signs of pests
Pest conducive conditions - pest opportunities inviting pests for food, water, and harborage
Key Elements of Inspection and Monitoring
Mouse poop on a spoon
The best way to know if or when pests are present is by regular inspection and monitoring
Cockroaches feeding on crumbs
Dawn H. Gouge, University of Arizona

## Slide 8
Where to look:
Dark shadowy corners
Hard to reach areas
Undisturbed places/ under and behind stationary items
Warm and/or wet places
Food storage and/or preparation areas
Waste collection containers and areas
Dropped ceilings
Key Elements of Inspection and Monitoring
Tiles in drop ceiling indicating roof or plumbing leak - Dawn H. Gouge, University of Arizona

## Slide 9
Where to look:
Warm walls with penetrations
Compressor motor voids in equipment
Unsealed floors and floor to wall junctures
Undisturbed containers
Cardboard boxes
Clutter
Under fixed equipment
Key Elements of Inspection and Monitoring
Dead rat found under fixed kitchen equipment – Dawn H. Gouge, University of Arizona

## Slide 10
Tools:
Monitoring traps
Bright flashlight
Hand lens
Key Elements of Inspection and Monitoring
Insect monitoring trap – Dawn H. Gouge, University of Arizona

## Slide 11
Document your observations while monitoring for pests in your food service area
Use a Pest Log Sheet and consider recording:
Pests
Signs of pests
Pest-conducive conditions
Frequency: as and when required during daily duties
Key Elements of Inspection and Monitoring
Insect monitoring trap – Shaku Nair, University of Arizona

## Slide 12
Sanitation and exclusion are basic steps in IPM
Good sanitation practices:
  Make sure all food-preparation areas, work surfaces, dishes and utensils and tools are completely clean of food residue by the end of the day
  Clean corners and hard-to-reach areas as frequently as possible, if not daily
Key Elements of Sanitation and Exclusion
Hard-to-reach places
in kitchens – Shujuan Li, University of Arizona

## Slide 13
Large, unwieldy and fixed equipment create hard-to-reach locations for cleaning or inspection - Dawn H. Gouge, University of Arizona
Hard-to-reach locations are dark, concealed places that may be covered and not subject to normal sweeping, mopping or brushing
Food and debris readily accumulate in difficult-to-reach locations, providing ideal habitat for pests
Hard-to-Reach Locations

## Slide 14
Corners where walls and floors meet, especially under and behind equipment or furniture, are ideal places for food, dirt and pest poop to accumulate
One of the hardest places to clean is the “back-leg zone” of equipment and fixtures
The “back-leg zone” - Dawn H. Gouge, University of Arizona
Hard-to-Reach Locations

## Slide 15
More Hard-to-Reach Locations
Under stoves and cooking ranges
Under covered floor drains
Under serving tables
Under sinks
Drains under fixed equipment
Dawn H. Gouge, University of Arizona

## Slide 16: 1.
Look for dark, damp, warm areas that are undisturbed or simply challenging to access
Unfortunately food debris often accumulates where pests go unnoticed
No matter how challenging, the areas must be carefully monitored and maintained free of food
Hard-to-Reach Locations
A hose behind fixed equipment creates a trap for debris and an area where grease and grime build up – Dawn H. Gouge, University of Arizona

## Slide 17: 1.
Floor Drains and Floor Sinks
Clean!
Not good
Just horrible!
Organic matter builds up and moth fly maggots breed in the matter that lines the drain
Often, food service staff clean from the floor up, and may not have the tools or training to clean floor drains
Drains must be maintained, so find out who is responsible for floor drain maintenance in your kitchen
Dawn H. Gouge, University of Arizona

## Slide 18
Occasional use equipment
Equipment that is used on special occasions, such as popcorn machines and concession stand equipment, may not be cleaned out regularly
These can be especially vulnerable to pests because they contain food residues
Popcorn machines have layers of grease on their walls and are difficult to clean – Dawn H. Gouge, University of Arizona

## Slide 19
Waste management is pest management:
  Use good quality trash cans made of strong plastic or steel for indoor use
  Keep the insides and undersides of trash cans clean – clean away from food preparation areas
  Use good quality trash bags that do not rip easily or need to be double bagged
  Consider freezing food remains that cannot be disposed of the same day
  If internal trash bins are on rollers, make sure the rollers and platform are also clean
Key Elements of Sanitation and Exclusion
Good quality trash bins and bags

## Slide 20
  Anything with food remains should be bagged, placed in trash cans, and taken to outside dumpsters before the end of each day
Key Elements of Sanitation and Exclusion
Avoid accumulating filled trash bags indoors - Jerry Jochim, Monroe County Community School Corporation

## Slide 21: 1.
  Keep dumpsters clean, covered and well-maintained
    Place dumpsters on a concrete or asphalt surface 30-50 feet away from building entryways
    Keep the area around the dumpster free of debris that can shelter pests
This dumpster is way too close to the kitchen entryway
Key Elements of Sanitation and Exclusion
Good placement of dumpsters, in separate enclosed area, but lids should be closed
Dawn H. Gouge, University of Arizona

## Slide 22
Left: Trash is haphazardly thrown into an over full dumpster, some falling onto the ground, if your receptacles are commonly overflowing, request a larger capacity dumpster
Right: All trash is secured in tied trash bags with no overflow, the lid will be closed at the end of the work day
Key Elements of Sanitation and Exclusion
Marc Lame, Indiana University

## Slide 23: 1.
Dumpsters should be rotated regularly for clean ones, lids should be kept closed at the end of the day
Your dumpster capacity should be sufficient, you should not have overflowing containers before collection
Discourage administrators from getting huge containers that are emptied only once a month, they become homes for feral cats, rats and all kinds of pests
Weekly collection is good, twice-weekly is better
Key Elements of Sanitation and Exclusion
Poorly managed dumpsters – Marc Lame, Indiana University
Notes: Objective 1

## Slide 24
Sanitation also involves proper storage of supplies/materials, this helps to:
Prevent pest-conducive conditions
Permit proper cleaning and inspection
Key Elements of Sanitation and Exclusion
Inspect, date, and organize supplies as they arrive
Cardboard covered wooden pallets are prone to support pests
Aluminum dunnage racks (left) are ideal, as you can see and clean beneath them
Dawn H. Gouge, University of Arizona

## Slide 25
  Proper storage practices
  Inspect deliveries for pests or signs of pests (e.g., chewed edges, pest droppings)
  Inspect for broken or leaking bags, containers, or cartons of food supplies, contain leaks or spills immediately and clean up thoroughly
  Avoid storing boxes and items up against the walls
  Leave 18-inch gaps under the lowest shelf so the floor can be cleaned underneath - at least 6 inches of clear space beneath equipment is mandatory
  Avoid using wooden pallets, milk crates, etc. to store things on for extended time
Key Elements of Sanitation and Exclusion

## Slide 26
Proper storage
Corrugations in cardboard boxes provide excellent harborage for cockroaches Avoiding as much cardboard as possible in storage areas is an important part of cockroach management
Problematic
Excellent
Jerry Jochim, Monroe County Community School Corporation

## Slide 27: Pest exclusion involves denying entryway to pests
Any sign of a pest should trigger a search for possible points of entry
Broken/torn wire-mesh screen covers of windows
Dry P-traps in drains
Worn out door-sweeps/weather stripping
Hitchhikers in deliveries
  Check for signs of pest presence (droppings, pests, webbing or holes in boxes and insect monitoring traps in food storage areas after a delivery)
Key Elements of Sanitation and Exclusion
This door needs new door sweeps and weather stripping – Dawn H. Gouge, University of Arizona

## Slide 28
Pest Exclusion Strategies/Tactics
Avoid propping doors open, it is a security risk and a pest invitation
Close gaps that provide access to pests, young mice can squeeze through a gap the size of a dime; young rats need nickel-sized gaps; American cockroaches can pass through a gap the width of a quarter
Avoid clutter, both inside your kitchen area and outside by external doorways
Keep food in sealed containers as much as possible
This space needs de-cluttering!
This door should be closed
Jerry Jochim, Monroe County Community School Corporation

## Slide 29
Replace worn door sweeps - Effective sweeps drastically reduce the number of invading pests and can cut pest complaints by as much as 65% in some situations
Seal gaps, cracks and crevices with suitable sealants
Cover windows and vents with wire mesh and replace with new wire mesh when broken
Pest Exclusion Strategies/Tactics
Torn wire-mesh on a vent – Dawn H. Gouge, University of Arizona

## Slide 30
P-traps in drains prevent gases, odors and insects from entering buildings
Keep them filled with water, dry P-traps create access to your building from the sewer for American cockroaches
Pest Exclusion Tools
Inspect drains periodically to prevent P-traps from drying out

## Slide 31: Thorough Cleaning Procedures
Most food service areas have fixed protocols for cleaning dishes and utensils, equipment, and work surfaces
However, there are some places that often get neglected
Shujuan Li, University of Arizona

## Slide 32: Thorough Cleaning Procedures
Drains
Organic matter builds up in drains, but can be scraped out with a scraper or stiff brush
Do this only after food has been put away, and before food preparation surfaces and equipment are sanitized to avoid contamination with Listeria and other pathogens sometimes found in drains
Once clear of organic build-up, regular maintenance with an enzyme or biological cleaner every month can help keep drains clean and free from clogging and unpleasant odors!

## Slide 33: Thorough Cleaning Procedures
Floor sink nets or dome strainers should also be cleaned regularly, some are dishwasher safe
Clean floor drain dome strainer
Floor drain strainer full of food
Dawn H. Gouge, University of Arizona

## Slide 34: Thorough Cleaning Procedures
Floors
Remove debris - A long handled dustpan and brush are useful for solid items, paper and other trash
To avoid contamination, never dry sweep in areas where food is on display or people are eating
A damp mop may be used to contain spilled liquids
Place food residues in garbage containers lined with good quality plastic liners that don’t tear easily
Tie plastic bags shut prior to placing them in a dumpster for removal to avoid spillage and reduce pest access

## Slide 35: Thorough Cleaning Procedures
Floors
If you hose down floors with water, avoid spraying water directly on motors and other electrical equipment
Do not allow moisture to come in contact with stored dry goods; moisture promotes mold growth
Physically remove food debris, remember some proteins coagulate at 140° to 145°F, making them more difficult to clean, excessively hot water or steam can bake proteins onto equipment much like an egg sticks to an ungreased frying pan

## Slide 36: Thorough Cleaning Procedures
Floors
Detergents are manufactured to do specific jobs Make your selection based on:
  The type of dirt to be removed
  The type of surface to be cleaned
  Water quality (hard or soft)
  Cleaning method (spray, foam, manual, etc.)
  Cost

## Slide 37: Thorough cleaning procedures
Floors
After applying detergent, rinse with clean potable water It is important to remove all detergent residue
Pay special attention to corners, floor joints and under equipment – Dawn H. Gouge, University of Arizona

## Slide 38
Keeping cleaning equipment in clean and in good working condition is equally important to avoid attracting pests
Food residues can accumulate in all of the following:
  Garbage receptacles
  Pans
  Brooms, dusters and brushes
  Mops and buckets
    Vacuum cleaners, polishers, scrubbers
Thorough cleaning procedures
These cleaning tools are filthy and need replacing – Dawn H. Gouge, University of Arizona

## Slide 39: Cleaning Equipment Maintenance and Storage
Emptying
Vacuum cleaners, floor scrubbers and other pieces of equipment usually need to be emptied of debris or chemicals before they are stored
Wiping Down, Washing and Rinsing
After use, each piece of equipment should be wiped down and, when appropriate, washed and rinsed to prevent build up of grit and grime

## Slide 40: Cleaning Equipment Maintenance and Storage
Storage
Once brooms, mops and other tools are clean, store the items on off-the-floor racks
Clean and dry mop heads may be stored in transparent plastic totes or on wire shelving
Avoid heaping mop heads on the floor or on solid shelving, they provide great harborage for spiders and cockroaches, and even nesting materials for mice
Store equipment off the floor and in a manner that will allow it to dry rapidly - Dawn H. Gouge, University of Arizona

## Slide 41: Thorough cleaning procedures
Above all, keep yourself clean and hygienic while working in your food service area!
If you physically remove a pest or article contacted by pests, double bag and place it in an outdoor garbage receptacle
Wash hands thoroughly after cleaning up, always before handling food and as you transition from task to task

## Slide 42: Thorough cleaning procedures
Wash hands in designated handwashing sinks
The handwashing station should include:
  Sink with hot water supply (at least 100oF)
  Handwashing soap
  Single-use paper towels for hand drying
  Trashcan for paper towels, disposable gloves, etc.
The use of nail brushes, hand sanitizer, and disposable gloves may be required

## Slide 43: Thorough cleaning procedures
Handwashing tips
  Rinse hands and arms up to the elbows
  Apply soap and lather for at least 15 seconds (sing the Happy Birthday song twice) – clean hands, arms, paying carful attention to finger nails
  Dry with paper towel
  If required apply hand sanitizer to completely dry hands
  If required put gloves on completely dry hands

## Slide 44: 2.
Learn more about IPM from experts
Ask questions, read IPM newsletters and participate in environmental health committee meetings
Consider discussing IPM and its advantages with your colleagues, principal and parents of students at suitable venues
Implementing IPM is easier with group support
Set an example and demonstrate your success with IPM
Effective Communication

## Slide 45
Food Service Staff and IPM
Dedicated food service staff automatically implement IPM as they go about their daily duties! You are already an expert
Clean serving area at a Middle School, Washington DC
- DC Central Kitchen

## Slide 46: Check In!
In this lesson you learned:
Key elements of sanitation and exclusion, including strategies, tactics and tools
Key elements of inspection and monitoring, including what and where to look, tools and frequency
Proper and thorough cleaning procedures for specific areas including drains, floors, corners, and hard-to-reach areas
Importance of effective communication and cooperation between food service staff and other school personnel
Congratulations, you have completed the School IPM for Food Service Staff Module!

## Slide 47: Resources
Food Service Checklist. IPM Institute of North America. http://www.ipminstitute.org/school_ipm_2015/foodservicechecklist.doc
Food Service IPM. Texas Cooperative Extension, Southwest Technical Resource Center http://schoolipm.tamu.edu/files/2010/11/Food_Service_IPMSmall.pdf
Get Tough on Pests in Food Service Areas. NC State University Cooperative Extension. http://schoolipm.ncsu.edu/documents/IPMforFoodserviceemployees.pdf
School IPM for Kitchen Staff. IPM Institute of North America. http://www.ipminstitute.org/School_IPM_Toolbox/School_IPM_for_kitchen_high_res_Aug_07.ppt
Safer Pest Control Project: IPM in Action http://www.spcpweb.org/factsheets/IPM_Picture_Tour_w_cover.pdf
Management of Ants in Childcare Settings. EPA. http://www2.epa.gov/sites/production/files/documents/Module09.pdf
Managing Mice and Rats In and Around Childcare. EPA. http://www2.epa.gov/sites/production/files/documents/Module05.pdf